## Slide 2
Content
Overview
How to Use LifeConnect PST
Some Important Things
1
2
3

## Slide 3
Overview
LifeConnet PST is a tool for update LifeConnect, which is a router within Life product.
Developed and maintained by SCD / Connected Objects / SWD / Tool & APP team.
Only support Windows now.
Communicates with device by ethernet. It needs a special RJ45 header, and a cable to connect host PC and LifeConnect.
Only ONE LifeConncet updated by the tool at once.
Recommend that host PC just has only one NIC (network card )

## Slide 4
How to Use LifeConnect PST
Insert USB power cable, RJ45 header into LifeConnect, connect host PC with network cable.
Edit LifeConnectFirmware.ini, if package file name is HB01_00_01.00_16_20161012.rar, then fill the RED/GREEN/BLUE text into CustomId, Version and BuildId separately.
Extract files from packages, put them into the folder which LifeConnectFirmware.ini locates.
Start LifeConnect PST, Click Button “Change Path”, navigates to the folder where LifeConnectFirmware.ini locates.
Click “Start” Button.
PST will try to find LifeConnect, it can change host PC NIC IP address, so user do not need set IP manually.
PST also checks LifeConnect version, if it is great than package version, PST will abort update. Click button beside “super mode”, enter password “54321”, this feature will disabled.

## Slide 5
Some Import Things
LifeConnect IP address can be in network segment 192.168.1 or 192.168.237 at normal mode, and runs telent server & dhcp server. At normal mode, LifeConnect is a router.
PST set static IP (192.168.1.10 or 192.168.237.10) for host PC, use telnet to login the gateway 192.168.1.1 or 192.168.237.1, which is just the IP of LifeConnect.
PST send command by telnet to Connect to get some import information. And check whether to update the Connect. It will send command to Connect to let it enter download mode.
Connect and host PC connect as P2P way. Host PC start TFTP server, and Connect use TFTP client to get firmware from the server. Connect always use 192.168.1.10. So when Connect enter download mode, PST must set host PC IP address to 192.168.1.10.

## Slide 6
Notes: Our brand is a smart move for the consumer